## Slide 1: OSI Models
GROUP - 4
K M Hasibudula (ROLL 01115)
Lt Col Jeenia Haque (ROLL 01116)
Mohammad Towhiduzzaman (ROLL 01117)
Md. Nasarul Hasan (ROLL 01118)
PRESENTED BY
Md. Nasarul Hasan

## Slide 2
01
02
03
LT COL JEENIA HAQUE
TRAINING DIRECTORATE
BANGLADESH ARMY
ROLL 01116
04
MD. NASARUL HASAN
PERSONAL OFFICER CABINET DIVISION
ROLL 01118
MD TOWHIDUZZAMAN
ADMINISTRATIVE OFFICER
M/O PUBLIC ADMINISTRATION
ROLL 01117
K M HASIBUDULA
FLIGHT LIEUTENANT
BANGLADESH AIR FORCE
ROLL 01115
OSI Models
GROUP - 4
PRESENTED BY
Md. Nasarul Hasan

## Slide 3
SEQUENCE
Introduction/What is the OSI model?
Layers of the OSI model
Data, Protocol & Activities
Interactive Session

## Slide 4
The Open Systems Interconnection (OSI) model is a conceptual model created by the International Organization for Standardization which enables diverse communication systems to communicate using standard protocols. On the other hand, OSI provides a standard for different computer systems to be able to communicate with each other.
The OSI model can be seen as a universal language for computer networking. It’s based on the concept of splitting up a communication system into seven abstract layers, each one stacked upon the last.
What is the OSI model?

## Slide 5
Layers of the OSI model
The seven abstraction layers of the OSI model can be defined as follows:
1. The Physical Layer
This layer includes the physical equipment involved in the data transfer, such as the cables and switches. This is also the layer where the data gets converted into a bit stream, which is a string of 1s and 0s.
2. The Data Link Layer
The data link helps data transfer between two devices on the SAME network. The data link layer takes packets from the network layer and breaks them into smaller pieces called frames.

## Slide 6
3. The Network Layer
The network layer is responsible for facilitating data transfer between two different networks. The network layer breaks up segments from the transport layer into smaller units, called packets, on the sender’s device, and reassembling these packets on the receiving device. The network layer also finds the best physical path for the data to reach its destination; this is known as routing.
4. The Transport Layer
Transport layer responsible for end-to-end communication between the two devices. This includes taking data from the session layer and breaking it up into chunks called segments before sending it to Network layer. The transport layer is also responsible for flow control and error control.

## Slide 7
5. The Session Layer
This is the layer responsible for opening and closing communication between the two devices. The time between when the communication is opened and closed is known as the session. The session layer ensures that the session stays open long enough to transfer all the data being exchanged, and then promptly closes the session in order to avoid wasting resources. The session layer also synchronizes data transfer with checkpoints.
6. The Presentation Layer
This layer is primarily responsible for preparing data so that it can be used by the application layer. This layer can also handle the encryption and decryption required by the application layer. Finally the presentation layer is also responsible for compressing data it receives from the application layer before delivering it to Session layer.

## Slide 8
7. The Application Layer
This is the only layer that directly interacts with data from the user. Software applications like web browsers and email clients rely on the application layer to initiate communications. the application layer is responsible for the protocols and data manipulation that the software relies on to present meaningful data to the user. Application layer protocols include HTTP as well as SMTP.

## Slide 9
Benefits of the OSI Model
Divides the aspects of network operations into less complex components.
Standardizes interfaces, enabling engineers to specialize design and development efforts to specific functions.
Facilitates modular engineering and prevents changes in one area from affecting others.
Ensures interoperability and allows network designers to choose the right networking devices.
Accelerates evolution and helps with testing and troubleshooting the network.

## Slide 10
01
To allow access to network resources
Application Layer
02
To translate, encrypt and compress data
Presentation Layer
03
To establish, manage and terminate session
Session Layer
04
To Provide reliable process-to-process; Massage delivery and error recovery
Transport Layer
05
To move packets from source to destination; to provide internetworking
Network Layer
06
To organize bits into frames; to provide Hop-to-hop delivery
Data Link Layer
07
To Transmit bits over a medium; to provide Mechanical and electrical specifications
Physical Layer
Data, Protocol & Activities

## Slide 11
INTERACTIVE SESSION

## Slide 12
THANK YOU

## Slide 13
OSI Layers | TCP/IP Suit | Activities
Application | Application Telnet, FTP, SMTP, HTTP, DNS, SNMP, Specific address etc. | To allow access to network resources
Presentation | Presentation | To translate, encrypt and compress data
Session | Session | To establish, manage and terminate session
Transport | Transport SCTP, TCP, UDP, Sockets and Ports address | To Provide reliable process-to-process; Massage delivery and error recovery
Network | Network IP, ARP/RARP, ICMP, IGMP, Logical address | To move packets from source to destination; to provide internetworking
Data Link | Data Link IEEE 802 Standards, TR, FDDI, PPP, Physical address | To organize bits into frames; to provide Hop-to-hop delivery
Physical | Physical Medium, Coax, Fiber, 10base, Wireless | To Transmit bits over a medium; to provide Mechanical and electrical specifications
Data, Protocol & Activities